## Slide 1
Lecturer: Prof. Dr. Tolga Girici
Email: tgirici@etu.edu.tr

## Slide 2: Circuit elements

## Slide 3: Circuit
An electrical circuit is an interconnection of electrical elements
element

## Slide 4: 1.2 Birimler

## Slide 5: 1.3 Yük ve Akım
Yük
Elektron
Proton
Akım

## Slide 6: 1.3 Yük ve Akım
Electric current is the time rate of change of charge. (A)
The amount of charge that passes through a point between time t0 and t is (C):

## Slide 7: 1.3 Yük ve Akım
Doğru akım
Alternatif akım

## Slide 8: Örnekler:
Example 1.1 How much charge is represented by 4,600 electrons?
Practice Problem 1.1: Calculate the amount of charge represented by 6.667 billion protons.
Example 1.2 The total charge entering a terminal is given by q = 5t sin 4πt mC. Calculate the current at t = 0.5 s.

## Slide 9: 1.4 Gerilim (Voltaj)
Voltage (potential difference) is the required energy to move a unit of charge between two points (V).
Voltage is always defined for two points.

## Slide 10: 1.5 Güç ve Enerji
Power is the time rate of change of energy (W),
Show that :

## Slide 11: 1.5 Güç ve Enerji
If the power is negative then the element is supplying power (ex: battery)
If it is positive than the element is consuming power (ex: resistor)

## Slide 12: 1.5 Güç ve Enerji
Energy is the total amount of work done in a time interval.

## Slide 13: Örnekler

## Slide 14: Örnekler

## Slide 15: 1.6 Circuit elements
Elektrik devresi devre elemanlarının çeşitli şekillerde bağlanması ile oluşur
There are two types of elements
  Active elements: Elements that generate energy
    Generators, batteries, amplifiers
  Passive elements: Elements that don’t generate energy
    Resistors, capacitors, inductors

## Slide 16: 1.6 Circuit elements
The source (energy source): The active element that generally deliver power to the circuit.
DC or Time varying
voltage source
DC voltage source

## Slide 17: 1.6 Circuit elements
The source (energy source): The active element that generally deliver power to the circuit.
Dependent sources are designated by a diamond shape.
Keep in mind that a voltage source comes with +- polarities whereas a current source with an arrow

## Slide 18: 1.6 Circuit elements
The dependent sources are divided in to 4 categories:
What type
of a source is that ?

## Slide 19: 1.6 Circuit Elements
Example: Calculate the power supplied or absorbed by each element.

## Slide 20: 1.6 Circuit Elements
Example: Calculate the power supplied or absorbed by each element.

## Slide 21: 1.7 Uygulamalar
Cathode Ray Tube (CRT)
  Karl Ferdinand Barun (1879)
  Vladimir Zworykin

## Slide 22: https://solaravm.com/elektrik-faturasi-nasil-hesaplanir

## Slide 23: Electrical Circuits
READ SECTION 1.8 CAREULLY !!